MULTIVIBRATOR CIRCUITS USING THE IC-555 TIMER

I. OBJECTIVES

- To determine the applications that can be obtained by combining a fast PF and a slow NF: astable multivibrator, monostable multivibrator.

- Understand how to use the IC-555 timer to obtain specific applications: astable multivibrator, monostable multivibrator, triangular wave signal generator.

II. COMPONENTS AND INSTRUMENTATION

We are using the experimental assembly equipped with the IC-555 timer and the IC 741, two potentiometers, capacitors and resistors of different values. For the assembly supply we use a dc voltage source. The visualization is done using a dual channel oscilloscope.

# III. PREPARATION

### Brief overview of the IC-555 timer

- Draw the internal block diagram of the IC-555 timer.

- Fill in the Table 1 that reflects the operation principle of the IC-555 (Vcc is the supply voltage).

The IC-555 can be considered equivalent to an inverting comparator with PF (with hysteresis), the input voltage being the voltage applied to the terminals Trigger and Threshold connected together. The thresholds of the comparator are internally fixed so we don’t have access to the PF. The VTC is shown in Fig. 1.

Table 1.

| Trigger terminal voltage | Threshold terminal voltage | Output voltage | Internal transistor state (off, aF, saturation) |
| --- | --- | --- | --- |
| < 1/3 V+ | < 2/3 V+ |  |  |
| < 1/3 V+ | >2/3 V+ | Forbidden |  |
| > 1/3 V+ | < 2/3 V+ |  |  |
| > 1/3 V+ | > 2/3 V+ |  |  |

Fig. 1. The VTC of the equivalent hysteresis comparator

P.1.The astable multivibrator circuit

For the circuit in Fig. 2:

- Find the value of the threshold voltage of the equivalent hysteresis comparator for: 	(1) vO=Vcc=15V;

(2) vO=0V.

- Plot vC2(t). Which are the charging and discharging paths of C2?

- vC2 is considered the feedback voltage corresponding to the NF. Comment on the evolution in time of the NF.

## P.2. Monostable multivibrator circuit triggered by sensor

The monostable multivibrator shown in Fig. 3 is triggered when the resistance of the sensor S drops to a value that causes the voltage at terminal Trigger to drop under 1/3 Vcc. This can be done by pressing with a finger both contacts of the sensor.

- Find the value of vO and the state of the discharging transistor from the IC-555 before and right after pressing the sensor S.

- Prove that the duration of the pulse generated at the output of the monostable circuit is:   TM=R2C2ln3=1,1R2C2.

- Find the possible range of values for TM.

## P.3. Square wave and triangular wave generator

In Fig. 4, a circuit which generates a square wave at the output of the IC-555 (vO) and a triangular wave across C2 is presented. Therefore the charging and discharging of C2 must be done with a constant current. The circuit that contains O.A., C3, R2, D is a constant current generator (I2), keeping the voltage across R2 approximately constant when vC2 varies. This is done using the bootstrap method.

When vC2=1/3Vcc, D is in on state and C3 is charging with 10V (2/3Vcc). When vC2 starts to increase, D goes in off state and vC3 remains approximately constant, 2/3Vcc. The I2 current is, in this case, provided by C3.

- Prove that I2 is constant (for the same cursor position of the potentiometer from R2).

- Prove that: I2=2Vcc/3R2.

Another constant current generator, I1, is formed from T1, R6 and R5, keeping the voltage across R4 constant when C2 is discharging.

- Prove that I1 is constant when C2 is discharging and it has the value: I1=4,75[V]/R4.

- Find the relation that expresses the period of the generated signals.

- For what positions of the potentiometers’ cursors the square wave signal has:

- maximum period?

- minimum period?

- maximum duty cycle?

- minimum duty cycle?

##### IV. EXPLORATIONS AND RESULTS

1. The astable multivibrator circuit

Explorations

Build the assembly shown in Fig. 2, connecting: PS+PJ, IN+ with PS, JR3, J1 with J2 and J4 with J5.

- Visualize simultaneously the voltages vO (OUT) and vC2. Modify the R2 (using the potentiometer) and find the minimum and maximum frequencies of output signal.

#### Results

- vO(t) and vC2(t). vC2(t) is the input voltage in the equivalent hysteresis comparator, and also the feedback voltage of the NF path.

- What are the values of the threshold voltages?

- The minimum and maximum period of generated signal.

- Did you know that this oscillator is called relaxation oscillator? What do you think, why?

Fig. 2. The astable multivibrator circuit

## 2. Monostable multivibrator circuit triggered by sensor

Explorations

Build the assembly shown in Fig. 3. Disconnect all jumpers and connect: DESC+ PS, PJ +S, PS with C2, J1 with J2 and J4 with J5.

- Visualize vO(t) after pressing the sensor with the finger (as explained before).

- Modify R2 from the 25kΩ potentiometer and examine its effect on the duration of the pulse generated at the output.

## Results

- vO(t) for the maximum and minimum values of R2.

- In what range can TM  vary? Compare with the result computed at P2.1.

- Those of you who are living in a block of flats, where do you think the applications of the monostable can be found in everyday life?

Fig. 3. Monostable multivibrator circuit triggered by sensor

## 3. Square wave and triangular wave generator

Explorations

Build the assembly shown in Fig. 4. Disconnect all jumpers and connect: PS+PJ, IN+ with PS, DESC+R4, J2 with J3 and J5 with J6.

- Make sure that the circuit generates the expected signals, namely vC2 -triangular wave and vO - square wave.

- Visualize vR2 and find the value of I2.

- Visualize simultaneously vO and vC2.

- Adjust the potentiometers one by one to derive the effect of each of them on the output signals.

- Set the potentiometers for the square wave signal (vO) to be of:

- maximum period

- minimum period

- maximum duty cycle

- minimum duty cycle

- For which of the above mentioned situations do we get a linearly variable (saw-tooth signal) voltage on C2?

Fig. 4. Signal generator

Results

- vC2(t) and vO(t).

- vR2(t)  and value of I2.

- The maximum and minimum period of the generated signal.

- The maximum and minimum duty cycle of the square wave signal.

- How do you explain the possibility to set-up the period and the duty cycle?

- Can the period and the duty cycle be modified independently?

- How should R2 and R4 be modified to obtain a linearly variable (saw-tooth signal) vC2(t)?

- Why do you think that the IC-555 is called timer?

REFERENCES

1. Oltean, G., Circuite Electronice, UT Pres, Cluj-Napoca, 2007, ISBN 978-973-662-300-4

2. Feştilă Lelia, Simion E., Miron C., Amplificatoare audio şi sisteme muzicale, Editura Dacia, Cluj-Napoca, 1990

3.  http://www.bel.utcluj.ro/dce/didactic/fec/fec.htm

Fig. 5. Experimental assembly