MOSFET LOGIC CIRCUITS

I. OBJECTIVES

- Finding out the logic function of some circuits with MOSFET

II. COMPONENTS AND INSTRUMENTATION

You will use the experimental assembly built with n-channel IRFZ24N MOSFETs and resistors. Because you will apply and measure both dc and ac voltages you will need a dc regulated voltage supply, a signal generator, a digital multimeter and a dual channel oscilloscope

III. PREPARATION

1.P. Logic inverter with MOSFET

The following logic convention is used: the high level of the voltage – “1” logic, the low level of the voltage – “0” logic.

For the n-channel IRFZ24N MOSFET, what is the value of the threshold voltage, VTh, and of (, according with the datasheet?

1.1.P Logic function

- Find the logic function of the circuit from Fig. 1.

1.2.P VTC

- Plot the VTC vY(vA) for the circuit in Fig. 1.

2.P. NAND logic circuit

- What is the electrical operating table for the circuit in Fig. 2? vA, vB ({0V, 5V}. What are the states (off or extreme conduction) of transistors TA and TB for all possible combinations of values of vA and vB?

- What is the truth table for the circuit in Fig. 2?

3.P. AND logic circuit

- What is the electrical operating table for the circuit in Fig. 3? vA, vB ({0V, 5V}. What are the states (off or extreme conduction) of transistors TA and TB for all possible combinations of values of vA and vB?

- What is the truth table for the circuit in Fig. 3?

4.P. NOR logic circuit

- What is the electrical operating table for the circuit in Fig. 4? vA, vB ({0V, 5V}. What are the states (off or extreme conduction) of transistors TA and TB for all possible combinations of values of vA and vB?

- What is the truth table for the circuit in Fig. 4?

5.P. OR logic circuit

- What is the electrical operating table for the circuit in Fig. 5? vA,vB ({0V, 5V}. What are the states (off or extreme conduction) of transistors TA and TB for all possible combinations of values of vA and vB?

- What is the truth table for the circuit in Fig. 5?

IV. EXPLORATION AND RESULTS

1. Logic inverter with MOSFET

1.1. Logic function

Exploration

Build the circuit in Fig. 1.

- At input A, apply a TTL signal with 1kHz frequency obtained from the signal generator.

- Using the calibrated oscilloscope in the Y-t mode you will visualise vA(t) and vY(t).

###### Results

- vA(t), vY(t).

- The truth table in which A and Y are the input and output logic variables.

- What is the logic function of the circuit?

Fig. 1. Logic inverter with MOSFET

1.2. VTC

Exploration

Use the circuit in Fig. 1.

- vA(t)=5 sin(2( 1000t) [V] [Hz]

- Using the oscilloscope in the Y-X mode you will visualise the VTC vY(vA)

Results

- VTC vY(vA). What is the value of the threshold voltage, based on the VTC from the oscilloscope?

2. NAND logic circuit

Exploration

Build the circuit in Fig. 2.

- vA, vB({0V;5V} in all possible combinations

- Measure vY with the dc voltmeter for all possible combinations of the two input voltages.

###### Results

- Electrical operating table containing vA, vB, vY, the off or exc states of TA and TB for the 4 possible combinations of vA and vB values from {0V;5V}

- Truth table with A, B logic inputs and Y logic output

- Is the logic function the same as the one determined at 2.P.?

Fig. 2. NAND logic circuit

3. AND logic circuit

Exploration

Build the circuit in Fig. 3.

- vA, vB({0V;5V} in all possible combinations

- Measure vY with the dc voltmeter for all possible combinations of the two input voltages.

###### Results

- Electrical operating table containing vA, vB, vY, the off or exc states of TA, TB, TC for the 4 possible combinations of vA and vB values from {0V;5V}

- Truth table with A, B logic inputs and Y logic output

- Is the logic function the same as the one determined at 3.P.?

Fig. 3. AND logic circuit

4. NOR logic circuit

Exploration

Build the circuit in Fig. 4.

- vA, vB({0V;5V} in all possible combinations

- Measure vY with the dc voltmeter for all possible combinations of the two input voltages.

###### Results

- Electrical operating table containing vA, vB, vY, the off or exc states of TA and TB for the 4 possible combinations of vA and vB values from {0V;5V}

- Truth table with A, B logic inputs and Y logic output

- Is the logic function the same as the one determined at 4.P.?

Fig. 4. NOR logic circuit

5. OR logic circuit

Exploration

Build the circuit in Fig. 5.

- vA, vB({0V;5V} in all possible combinations

- Measure vY with the dc voltmeter for all possible combinations of the two input voltages.

###### Results

- Electrical operating table containing vA, vB, vY, the off or exc states of TA, TB, TC for the 4 possible combinations of vA and vB values from {0V;5V}

- Truth table with A, B logic inputs and Y logic output

- Is the logic function the same as the one determined at 5.P.?

Fig. 5. OR logic circuit

REFERENCES

1. Oltean, G., Electronic Devices, Editura U.T. Pres, Cluj-Napoca, ISBN 973-662-220-7, 2006

2. Sedra, A. S., Smith, K. C., Microelectronic Circuits, Fifth Edition, Oxford University Press, ISBN: 0-19-514252-7, 2004

3. http://www.bel.utcluj.ro/dce/didactic/fec/

# Text boxes

A

RD

VDD=5V

Y

vA

vy

TA

TA

TB

A

B

VDD=5V

vB

vY

vA

RD

18kΩ

Y

TA

TB

A

B

VDD=5V

vB

vY

vA

RD1

18kΩ

Y

TC

RD2

18kΩ

TA

TB

A

B

VDD=5V

vB

vY

vA

RD

18kΩ

Y

TA

TB

A

B

VDD=5V

vB

vA

RD1

18kΩ

vY

Y

TC

RD2

18kΩ